## Slide 1
DISCOVER . LEARN . EMPOWER
Introduction to Operating System
Font size 24
UNIVERSITY INSTITUTEOF ENGINEERING
Bachelor of Engineering (Computer Science & Engineering)
Operating System (20CST/ITT-313)
Subject Coordinator: Er. Puneet Kaur(E6913)

## Slide 2: Distributed and Network Operating Systems
.

## Slide 3: Introduction
Distributed system is collection of loosely coupled processors interconnected by a communications network
Processors variously called nodes, computers, machines, hosts
  Site is location of the processor
Reasons for distributed systems
  Resource sharing
    sharing and printing files at remote sites
    processing information in a distributed database
    using remote specialized hardware devices
  Computation speedup – load sharing
  Reliability – detect and recover from site failure, function transfer, reintegrate failed site
  Communication – message passing

## Slide 4: A Distributed System

## Slide 5: Types of Distributed Operating Systems
Network Operating Systems
Distributed Operating Systems

## Slide 6: Network-Operating Systems
Users are aware of multiplicity of machines. Access to resources of various machines is done explicitly by:
  Remote logging into the appropriate remote machine (telnet, ssh)
  Remote Desktop (Microsoft Windows)
  Transferring data from remote machines to local machines, via the File Transfer Protocol (FTP) mechanism

## Slide 7: Distributed-Operating Systems
Users not aware of multiplicity of machines
  Access to remote resources similar to access to local resources
Data Migration – transfer data by transferring entire file, or transferring only those portions of the file necessary for the immediate task
Computation Migration – transfer the computation, rather than the data, across the system

## Slide 8: Distributed-Operating Systems (Cont.)
Process Migration – execute an entire process, or parts of it, at different sites
  Load balancing – distribute processes across network to even the workload
  Computation speedup – subprocesses can run concurrently on different sites
  Hardware preference – process execution may require specialized processor
  Software preference – required software may be available at only a particular site
  Data access – run process remotely, rather than transfer all data locally

## Slide 9: Network Structure
Local-Area Network (LAN) – designed to cover small geographical area.
  Multiaccess bus, ring, or star network
  Speed  10 – 100 megabits/second
  Broadcast is fast and cheap
  Nodes:
    usually workstations and/or personal computers
    a few (usually one or two) mainframes

## Slide 10: Depiction of typical LAN

## Slide 11: Network Types (Cont.)
Wide-Area Network (WAN) – links geographically separated sites
  Point-to-point connections over long-haul lines (often leased from a phone company)
  Speed  1.544 – 45 megbits/second
  Broadcast usually requires multiple messages
  Nodes:
    usually a high percentage of mainframes

## Slide 12: Communication Processors in a Wide-Area Network

## Slide 13: Network Topology
Sites in the system can be physically connected in a variety of ways; they are compared with respect to the following criteria:
  Installation cost - How expensive is it to link the various sites in the system?
  Communication cost - How long does it take to send a message from site A to site B?
  Reliability - If a link or a site in the system fails, can the remaining sites still communicate with each other?
The various topologies are depicted as graphs whose nodes correspond to sites
  An edge from node A to node B corresponds to a direct connection between the two sites
The following six items depict various network topologies

## Slide 14: Network Topology

## Slide 15: Video Links
https://www.youtube.com/watch?v=MtrcTjJfWSY https://www.youtube.com/watch?v=-OTP2O-UHhI

## Slide 16: References
https://www.unf.edu/public/cop4610/ree/Notes/PPT/PPT8E/CH15-OS8e.pdf
https://www.tutorialspoint.com/operating_system/os_security.htm
https://www.coursehero.com/file/19323929/Operating-System-Threats-and-Vulnerabilities/
https://www.cs.uic.edu/~jbell/CourseNotes/OperatingSystems/15_Security.html
https://devqa.io/security-threats-attack-vectors/
https://www.geeksforgeeks.org/system-security/
https://www.javatpoint.com/os-security-management