## Slide 1: Bluetooth security
Bluetooth technology allows devices to communicate with each other without cables or wires. Bluetooth relies on short-range radio frequency, and any device that incorporates the technology can communicate as long as it is within the required distance.
Bluetooth security is of paramount importance as devices are susceptible to a variety of wireless and networking attacking including denial of service attacks, eavesdropping, man-in-the-middle attacks, message modification etc.
Bluetooth security must also address more specific Bluetooth related attacks that target known vulnerabilities in Bluetooth implementations and specifications. These may include attacks against improperly secured Bluetooth implementations which can provide attackers with unauthorized access.

## Slide 2: Bluetooth security
Authentication: verifies the identification of devices that are communicating in the channel.
Confidentiality: protecting the data from the attacker by allowing only authorized users to access the data.
Authorization: only authorized have control over the resources.

## Slide 3: Security mode of bluetooth
Security mode 1: no secure mode,(there wont be any authentication or encryption in this mode. Bluetooth devices can easily be connected with the other devices. )
Security mode 2: service level security mode,(the management of the access control and interfaces with other protocols and device users is handled by the centralized security manager, it includes authentication, configuration, and authorization)
Security mode 3: link level security mode,(this is a built in security mechanism that offers the authentication encryption based on the security key shared by the pair of devices).

## Slide 4: Security issues
Bluejacking: Bluejacking is often not a major malicious security problem, although there can be issues with it, especially as it enables someone to get their data onto another person's phone, etc. Bluejacking involves the sending of a vCard message via Bluetooth to other Bluetooth users within the locality - typically 10 meters. The aim is that the recipient will not realize what the message is and allow it into their address book. Thereafter messages might be automatically opened because they have come from a supposedly known contact.
Bluebugging: This more of an issue. This form of Bluetooth security issue allows hackers to remotely access a phone and use its features. This may include placing calls and sending text messages while the owner does not realize that the phone has been taken over
Car Whispering: This involves the use of software that allows hackers to send and receive audio to and from a Bluetooth enabled car stereo system.
In order to protect against these and other forms of vulnerability, the manufacturers of Bluetooth enabled devices are upgrading the security to ensure that these Bluetooth security lapses do not arise with their products.